## Slide 1: I/O Disks

## Slide 2: Review
Memory-Mapped I/O
  Map all the control registers into the memory space
  Each control register is assigned a particular and unique memory address
DMA
  A memory address register
  A byte count register
  One or more control registers
  3 modes: Word-at-a-time, Block, Fly-by
Precise vs. Imprecise Interrupt
  Precise: Leave the machine in a well-defined state
    PC is saved in a known place
    All instructions before the one pointed to by the PC have fully executed
    No instruction beyond the one pointed to by the PC has been executed
    Execution state of the instruction pointed to by the PC is known
  Imprecise: Does not meet all requirements as precise

## Slide 3: Review
I/O Software
  Goals
    Device Independent, Error handling, Synchronous vs. Asynchronous, Buffering, Dedicated device allocation
  I/O with DMA
  Layers
    User level I/O software: pooling with daemon scheduling (Asynchronous)
    Device independent
      Uniform naming, Uniform interface, Independent block size
      Buffering
      Error handling, Dedicated device allocation
    Device Drivers: help OS control specified devices depending on standard interface
    Interrupt Handlers: handle interrupt to determine what the system should do

## Slide 4: Objectives…
Disks
  Disk Hardware
  Disk Formatting
  Disk Arm Scheduling Algorithms
  Error Handling
  Stable Storage

## Slide 5: DISKS Disk Hardware
Magnetic Disks
RAID
CD-ROMs
Disk Formatting

## Slide 6: DISKS RAID
Context
  Parallel processing is being used more and more to speed up CPU performance
  → Parallel I/O might be a good idea
  → The Patterson suggested six specific disk organization that could be used to improve disk performance, reliability, or both
Solution: using RAID
  Redundant Array of Inexpensive Disks or Redundant Array of Independent Disks
  A box full of disks is appeared as a single large disk
  All the drives are controlled using a RAID controller
  The data are distributed over the drive to allow parallel operation
  RAID consists of a SCSI controller → better performance & better reliability
  RAID have 6 schemes from level 0 through level 5

## Slide 7: DISKS RAID Level 0
Striping: the virtual single disk is divided up into strips of k sectors each to store data in distributing as
  Strip 0: sectors 0 to k – 1
  Strip 1: sectors k to 2k – 1
  Strip n: sectors nk to (n+1)k – 1
RAID 0 writes consecutive strips over the drives in RR
RAID 0 reads the data from consecutive strips as
  The software issues a command to read a data block
  RAID controller will bread this command into n separate commands, one for each of the n disks, and have them operate in parallel (→ the parallel I/O without the software knowing about it)
Advantages
  Works best with large request, the bigger the better
  Performance is excellent and the implementation is straightforward
Disadvantage
  Works worst with the OS asking for data one sector at a time
  No back up data/disk
Tanenbaum, Fig. 5-20.

## Slide 8: DISKS RAID Level 1
Duplicates all the disks (n primary disks and n backup disks)
On a write, every strip is written twice (slower than single disk)
On a read, either copy can be used, distributing the load over more drives (faster to twice)
The consistency is excellent (applying to crash or recovery)
Tanenbaum, Fig. 5-20.

## Slide 9: DISKS RAID Level 2
Works on the word or the byte
Split each byte of the single virtual disk into a pair of 4-bit nibbles
Then, add a Hamming code to each one to form a 7-bit word, of which bits 1, 2, and 4 were parity bits
All drives were synchronized in terms of arm position and rotational position
Last, it can write 7 bit Hamming coded word over all drive, 1 bit per drive
Advantages
  The total throughput was immense because in one sector time it could write max sectors worth of data (high data rate)
  Losing one drive did not cause problems because the Hamming code could handle at runtime
Disadvantages
  Requires all drives to be rotationally synchronized, and it only makes sense with a substantial number of drives
  Asks a lot of controller since it must do a Hamming checksum every time bit
Tanenbaum, Fig. 5-20.

## Slide 10: DISKS RAID Level 3
Is a simplified version of RAID level 2
A single parity bit is computed for each data word and written to a parity drive
The drives must be exactly synchronized since individual data words are spread over multiple drives
The drive crashes and a single parity gives only error detection, not error correction, it provides full 1 bit error correction since the position of the bad bit is known
If a drive crashes, the controller just pretends that its bit are 0s. If a word has a parity error, the bit from the dead drive must have been a 1
Advantage
  Offer very high data rates
Disadvantage
  The number of separate I/O requests per second they can handle is no better than for a single drive
Tanenbaum, Fig. 5-20.

## Slide 11: DISKS RAID Level 4 & Level 5
Work with strips, not individual words with parity and do not require synchronized drives
RAID 4
  Is like RAID 0, with a strip-for-strip parity written onto an extra drive
  If a drive crashes, the lost bytes can be recomputed from the parity drive by reading the entire set of drives
  Protects the loss of a drive but performs poorly for small updates. If one sector is changed, it is necessary to read all the drives in order to recalculate the parity, which must then be rewritten
  Optimization, the old user data and the old parity data is read and recompute the new parity from them → small update requires 2 reads and 2 writes
  Disadvantages: bottleneck due to the heavy load on the parity drive
RAID 5
  The bottleneck is eliminated by distributing the parity bits uniformly over all the drives, RR
  If the drive crashes, reconstructing the contents of the failed drive is a complex process

## Slide 12: DISKS RAID Level 4 & Level 5
Tanenbaum, Fig. 5-20.

## Slide 13: DISKS Disk Arm Scheduling Algorithms
How long disk drivers to read or write a disk block?
The time required is determined by 3 factors
  Seek time (the time to move the arm to the proper cylinder)
  Rotational delay (the time for the proper sector to rotate under the head)
  Actual data transfer time
For most disks, the seek time dominates the other two times, so reducing the mean seek time can improve system performance substantially

## Slide 14: DISKS First-Come, First-Served (FCFS)
Process request sequentially
Is intrinsically fair, but it generally does not provide the fastest service
Ex:
  A disk queue with requests for I/O blocks on cylinders in orders
  98, 183, 37, 122, 14, 124, 65, 67
  Assume that the disk head is initially at cylinder 53
  Result: 53 98 183 37 122 14 124 65 67
  Total head movement of 640 ((98-53)+(183-98)+(183-37)+(122-37)+(122-14)+(124-14)+(124-65)+(67-65))
  Average Seek length: 640/8 = 80

## Slide 15: DISKS Shortest Seek First (SSF)
Select the disk I/O request that requires the least movement of the disk arm from its current head position
Always choose the minimum seek time
Ex:
  A disk queue with requests for I/O blocks on cylinders in orders
  98, 183, 37, 122, 14, 124, 65, 67
  Assume that the disk head is initially at cylinder 53
  Result: 53 65 67 37 14 98 122 124 183
  Total head movement of 236 ((65-53)+(67-65)+(67-37)+(37-14)+(98-14)+(122-98)+(122-124)+(183-124))
  Average Seek Length: 236/8 = 29.5
Problems
  When the SSF is proceeding, the new request, that will have priority overall or next selection, appears. The arm will next go to the new request
  With a heavily loaded disk, the arm will tend to stay in the middle of the disk most of the time, so requests at either extreme will have to wait until a statistical fluctuation in the load causes there to be no request near the middle. → Request far from the middle may get poor services. The goals of minimal response time and fairness are in conflict here

## Slide 16: DISKS Elevator algorithms
Arm moves in one direction only, satisfying all outstanding requests until it reaches the last track in that direction
Direction is reversed
Requires the software to maintain 1 bit: the current direction bit, UP and DOWN
When a request finishes, the disk or elevator driver checks the bit.
  If it is UP, the arm or the cabin is moved to the next highest pending request
  If no requests are pending at higher positions, the direction bit is reversed
  When the bit is set to DOWN, the move is to the next lowest request position, if any

## Slide 17: DISKS Elevator algorithms
Ex:
  A disk queue with requests for I/O blocks on cylinders in orders
  98, 183, 37, 122, 14, 124, 65, 67
  Assume that the disk head is initially at cylinder 53
  Result with bit is DOWN:
  53 37 14 65 67 98 122 124 183
    Total head movement of 208 ((53-37)+(37-14)+(65-14)+(67-65)+(98-67)+(122-98)+(124-122)+(183-124))
    Average Seek Length: 208/8 = 26
  Result with bit is UP:
  53 65 67 98 122 124 183 37 14
    Total head movement of 299 ((65-53)+(67-65)+(98-67)+(122-98)+(124-122)+(183-124)+(183-37)+(37-14))
    Average Seek Length: 299/8 = 37.375
The elevator algorithms has is that given any collection of requests, the upper bound on the total motion is fixed: it is just twice the number of cylinders

## Slide 18: DISKS Elevator algorithms
A slight modification of elevator algorithms that has a smaller variance in response time is to always scan in the same direction
When the highest numbered cylinder with a pending request has been services, the arm goes to lowest number cylinder with a pending request and then continues moving in an upward direction
In effect, the lowest-number cylinder is thought of as being just above the highest-number cylinder
Ex:
  A disk queue with requests for I/O blocks on cylinders in orders
  98, 183, 37, 122, 14, 124, 65, 67
  Assume that the disk head is initially at cylinder 53
  Result: 53 65 67 98 122 124 183 14 37
  Total head movement of 153 ((65-53)+(67-65)+(98-67)+(122-98)+(124-122)+(183-124)+(37-14))
  Average Seek Length: 153/8 = 19.125

## Slide 19: DISKS Disk Arm Scheduling Algorithms
Some disks controller provide a way for the software to inspect the current sector number under the head
  If two or more requests for the same cylinder are pending, the driver can issue a request for the sector that will pass under the head next
  The controller can select any of its heads almost instantaneously
  If the seek time is much faster than the rotational delay
    Pending request should be sorted by sector number, and as soon as the next sector is about to pass under the head, the arm should be zipped over the right track to read or write it
  When several drives are present on the same controller, the OS should maintain a pending request table for each drive separately
    Whenever any drive is idle, a seek should be issued to move its arm to the cylinder where it will be needed next
    When the current transfer finishes, a check can be made to see if any drives are positioned on the correct cylinder
    If one or more are, the next transfer can be started on a drive that is already on the right cylinder
    If none of the arms is in the right place, the driver should issue a new seek on the drive that just completed a transfer and wait until the next interrupt to see which arm gets to its destination first

## Slide 20: DISKS Disk Arm Scheduling Algorithms
All the disk scheduling algorithms tacitly assume that the real disk geometry is the same as the virtual geometry
If it is not, then scheduling disk requests makes no sense because the OS cannot really tell whether cylinder 40 or cylinder 200 is closer to cylinder 39
On the other hand, if the disk controller can accept multiple outstanding requests, it can use these scheduling algorithms internally. In that case, the algorithms are still valid, but one level down, inside the controller

## Slide 21: DISKS Error Handling
Bad sector
  Sectors do not correctly read back the value just written to them
  If the defect is very small, the bad sector can be used
  Otherwise, the error cannot be masked
  Substituted the bad sector
    Controllers
      Remap the bad sector to the spare
      Shift all the sectors up one
      The information about the substitution of the bad sector is kept track through internal tables or by rewriting the preambles to give the remapped sector numbers (besides, the data must be copied)
      When defect occurs at normal operation (may be specks of dust), if getting repeated errors on a certain sector, controller can switch to a spare before the sector has died completely
    OS
      Must first acquire a list of bad sectors, either reading them from the disk, or simply testing the entire disk itself
      Once it knows, the OS can build remapping tables

## Slide 22: DISKS Error Handling
Bad sector (cont)
  Problem: backup
    File to file: OS has to hide the bad block file so well that even a backup utility cannot find it
    Sector to Sector: impossible except that the only hope that the backup program has enough smarts to give up after 10 failed reads and continue with next sector
Seek errors
  Caused by mechanical problems in the arm occur
  The controller keeps track of the arm position internally
  To perform seek, it issues a series of pulses to the arm motor, on pulse per cylinder, to move the arm to the new cylinder.
  When the arm gets to its destination, the controller reads the actual cylinder number from the preamble of the next sector.
  If the arm is in the wrong place, a seek error has occurred
  Solutions
    Most hard disk controller correct seek errors automatically, but most floppy controllers just set an error bit and leave the rest to the driver.
    The driver handles this error with particular command to move the arm as far out as it will go and reset the controller’s internal idea of the current cylinder to 0
    If it does not, the driver must be repaired

## Slide 23: DISKS Stable Storage
A system has the following properties
  When a write is issues to it, the disk either correctly writes the data or it does nothing, leaving the existing data intact
  Is implemented in software
  The goal is to keep the disk consistent at all costs
Assume that the errors can not detected at the disk written (the errors can be detected on a subsequent read)
Assume that a correctly written sector can spontaneously go bad and become unreadable → small enough to ignore (so rarely)
Assume the CPU can fail or just stops.
  Any disk writes in process at the moment of failure also stops, leading to incorrect data in one sector and an incorrect ECC that can later be detected.
  Under all these conditions, stable storage can be made 100% reliable in the sense of writes either working correctly or leaving the old data in place

## Slide 24: DISKS Stable Storage
Uses a pair of identical disks with the corresponding blocks working together to form one error-free block
In the absence of errors, the corresponding blocks on both drives are the same
Either one can be read to get the same result
Three operations
Stable writes
  Write block on drive 1, then reading it back to verify written correctly
  If not correctly, the write and reread are done until they work
  After consecutive failures, the block is remapped onto a spare and the operation repeated until it succeeds, no matter how many spare have to be tried
  After succeeded on drive 1, the driver 2 is written and reread until it succeeds
  In the absence of CPU crashes, when a stable write completes, the block has correctly been written onto both drives and verified on both of them

## Slide 25: DISKS Stable Storage
Stable reads
  First read block on drive 1 in n times
  If all of these give bad ECCs, reading on drive 2
  Given the fact that a successfully stable write leaves 2 good copies of the block behind, and our assumption that the probability of the same block spontaneously going bad on both drives in a reasonable time interval is negligible, a stable read always succeeds
Crash recovery
  After a crash, a recovery program scans both disks comparing corresponding blocks
  If a pair of blocks are both good and the same, nothing is done
  If one of them has an ECC error, the bad block is overwritten with the good blocks
  If a pair of blocks are good but different, the block from driver 1 is written onto drive 2
In the absence of CPU crash, stable storage always works because stable writes always write two valid copies of every block and spontaneous errors are assumed never to occur both corresponding blocks at the same time

## Slide 26: DISKS Stable Storage
Tanenbaum, Fig. 5-31.

## Slide 27: DISKS Stable Storage
Optimizations and improvements
  Comparing all the blocks pairwise after a crash is doable, but expensive
  A huge improvement is to keep track of which block was being written during a stable write so that only one block has to be checked during recovery
  In system with Nonvolatile RAM,
    The stable write can put the number of block in RAM before starting the write
    After completed, the block number in RAM is overwritten with an invalid block.
    Under these conditions, after a crash, the recovery can check RAM to see if a stable write happened to be in progress during the crash
    → two copies of the block can then be checked for correctness and consistency
  If nonvolatile RAM is not available
    At the start of a stable write, a fixed disk block on drive 1 is overwritten with the number of block to be stably written. Then read back and verify.
    If is so, write 2 and verify. After completed, both blocks are overwritten with an invalid block number and verified
    → it is easy to determine whether or not a stable write was in progress during the crash
    → requires extra disk operations to write a stable block → should be used exceeding sparingly

## Slide 28: Summary
Disks
Q&A

## Slide 29: Next Lecture
Clock
  Hardware and Software
  Soft Timers
User Interfaces
  Input & Output Software